## Slide 1: Chapter Two Data Representation and Basics of Computer architecture

## Slide 2: Data Representation
Computers use digital representation
Based on a binary system (uses on/off states to represent 2 digits).
ALL data (no matter how complex) must be represented in memory as binary digits (bits).

## Slide 3: Number systems and computers
Computers store all data as binary digits, but we may need to convert this to a number system we are familiar with.
Computer programs and data are often represented (outside the computer) using octal and hexadecimal number systems because they are a short hand way of representing binary numbers.

## Slide 4: Number Systems - Decimal
The decimal system is a base-10 system.
There are 10 distinct digits (0 to 9) to represent any quantity.
For an n-digit number, the value that each digit represents depends on its weight or position.
The weights are based on powers of 10.
1024 = 1*103 + 0*102 + 2*101 + 4*100 = 1000 + 20 + 4

## Slide 5: Number Systems - Binary
The binary system is a base-2 system.
There are 2 distinct digits (0 and 1) to represent any quantity.
For an n-digit number, the value of a digit in each column depends on its position.
The weights are based on powers of 2.
10112 = 1*23 + 0*22 + 1*21 + 1*20 =8+2+1 =1110

## Slide 6: Number Systems - Octal
Octal and hexadecimal systems provide a shorthand way to deal with the long strings of 1’s and 0’s in binary.
Octal is base-8 system using the digits 0 to 7.
To convert to decimal, you can again use a column weighted system 75128 = 7*83 + 5*82 + 1*81 + 2*80 = 391410
An octal number can easily be converted to binary by replacing each octal digit with the corresponding group of 3 binary digits
75128 = 1111010010102

## Slide 7: Number Systems - Hexadecimal
Hexadecimal is a base-16 system.
It contains the digits 0 to 9 and the letters A to F (16 digit values).
The letters A to F represent the unit values 10 to 15.
To convert to decimal, use a weighted system with powers of 16.

## Slide 8: Number Systems - Hexadecimal
Conversion to binary is done the same way as octal to binary conversions.
This time though the binary digits are organized into groups of 4.
Conversion from binary to hexadecimal involves breaking the bits into groups of 4 and replacing them with the hexadecimal equivalent.

## Slide 9: Example #1 Value of 2001 in Binary, Octal and Hexadecimal

## Slide 10: Example #2 Conversion: Binary -> Octal ->Hexadecimal

## Slide 11: Decimal to BaseN Conversions
To convert from decimal to a different number base such as Octal, Binary or Hexadecimal involves repeated division by that number base
Keep dividing until the quotient is zero
Use the remainders in reverse order as the digits of the converted number

## Slide 12: Example #3 Decimal to Binary 1492 (decimal) = ??? (binary) Repeated Divide by 2

## Slide 13: BaseN to Decimal Conversions
Multiply each digit by increasing powers of the base value and add the terms
Example: 101102 = ??? (decimal)

## Slide 14: Data Representation
Computers store everything as binary digits. So, how can we encode numbers, images, sound, text ??
We need standard encoding systems for each type of data.
Some standards evolve from proprietary products which became very popular.
Other standards are created by official industry bodies where none previously existed.
– Some example encoding standards are ?

## Slide 15: Alphanumeric Data
Alphanumeric data such as names and addresses are represented by assigning a unique binary code or sequence of bits to represent each character.
As each character is entered from a keyboard (or other input device) it is converted into a binary code.
Character code sets contain two types of characters:
  – Printable (normal characters)
  – Non-printable. Characters used as control codes.
    CTRL G (beep)
    CTRL Z (end of file)

## Slide 16: Alphanumeric Codes
Characters are represented internally by these 8-bit binary codes.
An 8-bit memory word can thus store one character.
A 16-bit memory word is usually divided into two 8-bit segments or bytes.
Each of which can store a single character. Similarly, a 32-bit memory word can store four characters.
Character strings of length greater than the number of bytes in a word are stored in two or more consecutive words.
There are 3 main coding methods in use:
    ASCII, EBCDIC ,Unicode .

## Slide 17: ASCII (American Standard Code for Information Interchange)
7-bit code (128 characters)
has an extended 8-bit version
used on PC’s and non-IBM mainframes
widely used to transfer data from one computer to another

## Slide 18: ASCII character set (Sample)

## Slide 19: EBCDIC (Extended Binary Coded Decimal Interchange Code).
An 8-bit code (256 characters)
Different collating sequence to ASCII
used on mainframe IBM machine
Both ASCII and EBCDIC are 8 bit codes inadequate for representing all international characters
  – Some European characters
  – Most non-Alphabetic languages
  eg Mandarin, Kanji, Arabic, etc…

## Slide 20: Unicode
New 16 bit standard - can represent 65,536 characters
Of which 49,000 have been defined
  – 6400 reserved for private use
  – 10,000 for future expansions
Incorporates ASCII-7
Example - Java code:
char letter = ‘A’;
char word[ ] = ‘YES’;
stores the values using Unicode characters
Java VM uses 2 bytes to store one Unicode character.

## Slide 21: Numeric Data
Need to perform computations
Need to represent only numbers
Using ASCII coded digits is very inefficient
Representation depends on nature of the data and processing requirements
Display purposes only (no computations): CHAR
  • PRINT 125.00
  – Computation involving integers: INT
  • COMPUTE 16 / 3 = 5
  – Computation involving fractions: FLOAT
  • COMPUTE 2.001001 * 3.012301 = 6.0276173133

## Slide 22: Representing Numeric Data
Stored within the computer using one of several different numeric representation systems
Derived from the binary (base 2) number system.
We can represent unsigned numbers from 0-255 just using 8 bits
Or in general we can represent values from 0 to 2N -1 using N bits.
The maximum value is restricted by the number of bits available (called Truncation or Overflow)
However, most programming languages support manipulation of signed and fractional numbers.
  How can these be represented in binary form?

## Slide 23: Representing Numeric Data
Range of Values 0 to 2N-1 in N bits

## Slide 24: Integer Representation
UNSIGNED representing numbers from 0 upwards or SIGNED to allow for negatives.
In the computer we only have binary digits, so to represent negative integers we need some sort of convention.
Four conventions in use for representing negative integers are:
        – Sign Magnitude
        – 1’s Complement
        – 2’s Complement
        – Excess 128

## Slide 25: Negative Integers – Sign Magnitude
Simplest form of representation
In an n-bit word, the right most n-1 bits hold the magnitude of the integer
Example:
  – +6 in 8-bit representation is: 00000110
  – -6 in 8-bit representation is: 10000110
  Disadvantages
    – arithmetic is difficult
    – Two representations for zero
        • 00000000
        • 10000000

## Slide 26: Binary Arithmetic Binary Addition
Addition in binary is precisely analogous to addition in decimal.
Working from the write, if the sum of 2 digits produces a 2 digit result, the digit on the right is written down and the digit on the left is added to the next column to the left.

## Slide 28: Binary Subtraction
Recall that in decimal subtraction one subtracts a decimal digit from a smaller decimal digit by borrowing 1 from the term on the left.
Binary subtraction can be accomplished similarly. The borrowed 1 and the 0 of the location involved combine to form (10)2.
Thus, if there is a digit on the left, 0 - 1 becomes 10 -1 = 1, with a 1 borrowed from the left.

## Slide 30: Binary Multiplication

## Slide 32: Binary Division
Binary division is similar in procedure to decimal division. The placement of the binary point is exactly the same as the placement of the decimal point in decimal division.
Example: Evaluate 00101010 ÷ 110
Solution: applying the usual division procedure, we obtain:

## Slide 34: Negative Integers – One’s (1’s) Complement
Computers generally use a system called “complementary representation” to store negative integers.
Two basic types - ones and twos complement, of which 2’s complement is the most widely used.
The number range is split into two halves, to represent the positive and negative numbers.
Negative numbers begin with 1, positive with 0.

## Slide 35: Negative Integers – One’s (1’s) Complement
To perform 1’s complement operation on a binary number, replace 1’s with 0’s and 0’s with 1’s (ie Complement it!)
+6 represented by: 00000110
-6 represented by: 11111001
Advantages: arithmetic is easier (cheaper/faster electronics)
Fairly straightforward addition – Add any carry from the Most Significant (left-most) Bit to Least Significant (right-most) Bit of the result
For subtraction – form 1’s complement of number to be subtracted and then add
Disadvantages : still two representations for zero 00000000 and 11111111 (in 8-bit representation)

## Slide 36: Negative Integers – Two’s (2’s) Complement
To perform the 2’s complement operation on a binary number
– replace 1’s with 0’s and 0’s with 1’s (i.e. the one's complement of the number)
– add 1
    +6 represented by: 00000110
    -6 represented by: 11111010
Advantages:
  – Arithmetic is very straightforward
  – End Around Carry is ignored
only one representation for zero (00000000)

## Slide 37: Negative Integers – Two’s (2’s) Complement
Two’s Complement
–To convert an integer to 2’s complement
Take the binary form of the number
00000110 (6 as an 8-bit representation)
Flip the bits: (Find 1’s Complement)
11111001
Add 1 11111001 +1 = 11111010 (2’s complement of 6)
Justification of representation: 6+(-6)=0?
00000110 (6)
+11111010 (2’s complement of 6)
100000000 (0)

## Slide 38: Negative Integers – Two’s (2’s) Complement
Properties of Two’s Complement
–The 2’s comp of a 2’s comp is the original number
00000110 (6)
11111010 (2’s comp of 6)
00000101
+1
00000110 (2’s comp of 2’s comp of 6)
–The sign of a number is given by its MSB
The bit patterns:
00000000 represents zero
0nnnnnnn represents positive numbers
1nnnnnnn represents negative number

## Slide 39: Negative Integers – Two’s (2’s) Complement
•Addition
–Addition is performed by adding corresponding bits
00000111 ( 7)
+00000101 (+5)
00001100 (12)
•Subtraction –Subtraction is performed by adding the 2’s complement
–Ignore End-Around-Carry
00001100 (12)
+11111011 (-5)
100000111 ( 7)

## Slide 40: Negative Integers – Two’s (2’s) Complement
•Interpretation of Negative Results
00000101 ( 5)
+11110100 (-12)
11111001 ( )
–Result is negative
MSB of result is 1 so it is a negative number in 2’s complement form
–Negative what?
Take the 2’s comp of the result to find out since the 2’s comp of a 2’s comp is the original number
–Negative 7 the 2’s complement of 11111001 is 00000111 or 710

## Slide 41: Binary Fractions
The Binary Point
  – Digits on the left = +ve powers of 2
  – Digits on the right = –ve powers of 2

## Slide 42: Integer Overflow
Problem: word size is fixed, but addition can produce a result that is too large to fit in the number of bits available.
This is called overflow.
If two numbers of the same sign are added, but the result has the opposite sign then overflow has occurred
Overflow can occur whether or not there is a carry
Example:
01000000 ( +64) 10000000 (-128)
01000001 ( +65) 11000000 ( -64)
10000001 (-127) 01000000 ( +64)

## Slide 43: Next Class
Basics of digital logic gates and Boolean algebra